## Slide 1: Specimen Collection, Packaging and Transport Guidelines for 2019 novel Corona virus
State Institute of Health & Family Welfare
Rajasthan

## Slide 2: Responsibilities
The clinician should decide necessity for collection of clinical specimens for laboratory testing of 2019-nCoV only after following the case definition as given by the health authorities, Government of India.
Appropriate clinical sample need to be collected by laboratory personnel/ health care worker trained in specimen collection in presence of a clinician.
By following all biosafety precautions and using personal protective equipment (PPEs), clinical samples need to be sent to the designated laboratory by following standard triple packaging.

## Slide 3: Selection of patient
Any person
  present with Severe Acute Respiratory Illness (SARI);
  has travel history;
  disease in healthcare worker working in an environment of SARI patients;
  unusual or unexpected clinical course, especially sudden deterioration despite appropriate treatment; should be urgently investigated.
Updated case definition need to be followed as per MOHFW, Govt of India which is available on the website www.mohfw.gov.in

## Slide 4: Specimen collection details (Adapted from the WHO guidelines on 2019-nCoV)
Specimen type | Collection materials | Transport to laboratory | Storage till testing | Comment
Nasopharyngeal and oropharyngeal swab | Dacron or polyester flocked swabs* | 4 °C | ≤5 days: 4 °C >5 days: -70 °C | The nasopharyngeal and oropharyngeal swabs should be placed in the same tube to increase the viral load.
Bronchoalveolar lavage | sterile container* | 4 °C | ≤48 hours: 4 °C >48 hours: –70 °C | There may be some dilution of pathogen, but still a worthwhile specimen
*For transport of samples for viral detection, use VTM (viral transport medium) containing antifungal and antibiotic supplements. Avoid repeated freezing and thawing of specimens.

## Slide 5: Specimen collection details (Adapted from the WHO guidelines on 2019-nCoV)
Specimen type | Collection materials | Transport to laboratory | Storage till testing | Comment
Tracheal aspirate, nasopharyngeal aspirate or nasal wash | sterile container* | 4 °C | ≤48 hours: 4 °C >48 hours: –70 °C | Not applicable
Sputum | sterile container | 4 °C | ≤48 hours: 4 °C >48 hours: –70 °C | Ensure the material is from the lower respiratory tract
*For transport of samples for viral detection, use VTM (viral transport medium) containing antifungal and antibiotic supplements. Avoid repeated freezing and thawing of specimens.

## Slide 6: Specimen collection details (Adapted from the WHO guidelines on 2019-nCoV)
Specimen type | Collection materials | Transport to laboratory | Storage till testing | Comment
Tissue from biopsy or autopsy including from lung | sterile container with saline | 4 °C | ≤24 hours: 4 °C >24 hours: –70 °C | Autopsy sample collection preferably to be avoided
Serum (2 samples – acute and convalescent) | Serum separator tubes (adults: collect 3-5 ml whole blood) | 4 °C | ≤5 days: 4 °C >5 days: –70 °C | Collect paired samples: acute – first week of illness convalescent – 2 to 3 weeks later

## Slide 7: Specimen labeling and processing
Personal protective equipment (apron, hand gloves, face shield, N95 Masks etc.) need to be used and all biosafety precautions should be followed so as to protect individuals and the environment.
Proper labelling (name/age/gender/specimen ID) need to be done on specimen container and other details of sender (name/address/phone number) on the outer container by mentioning “To be tested for 2019-nCoV”

## Slide 8: Requirements for Clinical Samples Collection, Packaging and Transport
1. Sample vials and Virus
Transport Medium (VTM)
2. Adsorbent material
(cotton, tissue paper), paraffin, seizer, cello tape
3. A leak-proof secondary container (e.g.,
ziplock pouch, cryobox, 50 mL centrifuge tube, plastic container)
4. Hard-frozen Gel Packs
5. A suitable outer container (e.g., thermocol box, ice-box, hard-board box)
(minimum dimensions: 10 x 10 x 10 cm)

## Slide 9: Procedure for Specimen Packaging and Transport
1. Use PPE while handling specimen
2. Seal the neck of the sample vials using parafilm
3. Cover the sample vials using absorbent material

## Slide 10: Procedure for Specimen Packaging and Transport
4. Arrange primary
container (vial) in secondary container
5. Placing the centrifuge tube inside a zip-lock pouch
6. Placing the zip-lock pouch inside a sturdy plastic container and seal the neck of the container

## Slide 11: Procedure for Specimen Packaging and Transport
7. Using a thermocol box as
an outer container and placing the secondary container within it, surrounded by hard- frozen gel packs
7. Using a hard card-board box
as an outer container and placing the secondary container and the gel packs
8. Placing the completed
Specimen Referral Form (available on www.niv.co.in) and request letter inside a leak-proof, zip-lock pouch

## Slide 12: Procedure for Specimen Packaging and Transport
9. Securing the zip-lock
pouch with the Specimen Referral Form on the outer container
10. Attaching the labels:
Senders’ address, contact number; Consignee’s address /contact number;
Biological substance- Category B;
‘UN 3373’; Orientation label, Handle with care

## Slide 13: Documents to accompany
Packaging list/proforma Invoice
Air way bill (for air transport) (to be prepared by sender or shipper)
Value equivalence document (for road/rail/sea transport)
Note:
1. A vaccine-carrier/ice-box can also be used as an outer container
2. The minimum dimensions of the outer container should be 10 x 10 x 10 cm (length x width x height)

## Slide 14: Source of above information
https://www.mohfw.gov.in/pdf/5Sample%20collection_packaging%20%202019-nCoV.pdf